Physics 104					Exam IVa						2 May 2011

Name _________________________________ [1 or 0 point]

Select and circle the best answer for each of the following questions.
[zero or one point each]

1.	The intensity of light is defined as power per unit area.  So what are the SI units of 	intensity?

a) Watts		b) Joule/m2		c) Watts/m2		d) Volts

2.	The frequency of a wave is expressed in cycles/sec.  The SI unit of frequency is the _____.

a) Mertz		b) Hertz		c) Hartz		d) cps

3.	On the electromagnetic spectrum, visible light waves have wavelengths ___________ do 	microwaves.

a) longer than		b) the same as		c) shorter than		d) rounder than

4.	The shorter the wavelength, the more light is refracted.  This phenomenon is called ______.

a) perversion		b) reversion		c) inversion			d) dispersion

5.	Light travels __________ in a material medium than it travels in a vacuum.

a) faster					b) slower

c) neither slower not faster		d)  sometimes faster and sometimes slower

Select and circle the best answer for each of the following questions.  Show your work. [zero, one, or two points each]

6.	The green light [wavelength = ] of a diode laser moves with a speed of 	 in vacuum.  If its frequency is unchanged when the light enters a glass prism, 	what is its wavelength in the glass? [n = 1.33]

a) 		b) 		c) 		d)

7.	An object is 5.0 cm to the left 	of a convex mirror.  The 	focal length is -3.00 cm.  The 	height of the object is 1.6 cm.  	The magnification of the 	image is

a) 0.38

b) 2.67

c) -0.38

d) -2.67

8.	In the diagram to the right, a light ray 	encounters an interface and is refracted. 	Evaluate the angle of refraction.

a) 		b)

c) 		d)

9.	Parallel light rays pass through a small opening of 	width a.  A diffraction pattern is formed on a 	screen that is a distance R away from the small 	opening.  The center of the first dark fringe occurs	 at the point P on the screen.  Determine the 	wavelength of the light waves, if

a) 		b)

c) 		d)

10.	Describe the image formed by 	the convex refracting surface as 	shown in the sketch.  Assume 	that and ,

and .

a) real, inverted

b) virtual, inverted

c) real, erect

d) virtual, erect

Work the following problem(s). Show your work.  [Ten points each]

11.	Consider an object located to the left of a flat interface between two media, as shown in the 	diagram.  Where does the object appear to be to an observer standing to the right of the 	interface?  Where is the image seen by the observer on the left side?

[; ;]

12.	An object stands in front of a concave mirror.  Trace some representative rays to locate 	the image formed by the mirror.  Describe the image formed by this surface.  The letter C 	indicates the center of curvature of the mirror.

R = 10 cm, s = 15 cm.

Constants & miscellaneous formulae

Electric Force, Field, and Flux

Potential Energy, Voltage & Capacitance

Current and Circuits

Magnetic Fields

Biot-Savart

infinite line    					on axis of ring(s)

Ampere’s Law				inside a solenoid

Force on a charged particle		      force on a current element

Force on a long straight wire			torque on a current loop

Magnetic flux in general			transformer equation

Loop(s)			Rotating coil

Faraday’s “Law”	E = 			EMF along a moving wire	E =

Optics

“Law” of Reflection				Snell’s “Law”

Mirrors & lenses							spherical mirror

Refracting surfaces	spherical   		
				plane surface

Diffraction		dark fringes at   		diffraction angle

2-slit interference		bright fringes at                or