Physics 309			Charge to Mass Ratio of the Electron		      Fall 2013

A charged particle, such as an electron, that is moving in a uniform magnetic field will experience a magnetic force.

is the velocity of the electron and  is the magnetic field.  The force is perpendicular to the velocity, so the electron will follow a circular path at a constant speed, i.e., uniform circular motion.  In the context of Newton’s Second “Law” with ,

is the charge-to-mass ratio of the electron.

Electrons are accelerated by a specified voltage in a vacuum tube.  A known magnetic field is applied to the tube.  A small amount of mercury vapor in the tube makes the circular path followed by the electrons visible; the radius of the circle can be measured.

The velocity of the electron is related to the accelerating voltage thusly:

Whence,

.

The magnetic field is produced by a pair of Helmholtz coils.

is the permeability of empty space, N is the number of loops of wire in each coil, I is the current in the coils, and a is the radius of the coils.

Finally, the working equation for the experimental exercise is

.

That glob of units in the denominator are the units of .  See the line preceding Eqn 6 in the apparatus write-up.

At this point, we follow the directions in the documentation supplied with the e/m apparatus.

Note that the accepted value of e/m is 1.76x1011C/kg.  When the instructor performed the experiment rather hurriedly, he obtained 1.85x1011 C/kg.  We hope we can do better by being more careful.

Diagram of the electrical connections, as the apparatus is set up on the table.  The r, b, & b refer to red, brown, & brown wires entering the vacuum tube.

Diagram of the two parts of the apparatus.  The e/m tube on the left, and the Helmholtz Coil circuit on the right.

Sample data table:

| Crossbar | D | r | V | I1 | I2 | I | e/m |
| --- | --- | --- | --- | --- | --- | --- | --- |