Physics 103			Assignment 5

5.4.	Identify:   For the maximum tension, the patient is just ready to slide so static friction is at its maximum and the forces on him add to zero.

Set Up:   (a) The free-body diagram for the person is given in Figure 5.4a. F is magnitude of the traction force along the spinal column and  is the person’s weight. At maximum static friction,

(b) The free-body diagram for the collar where the cables are attached is given in Figure 5.4b. The tension in each cable has been resolved into its x and y components.

Figure 5.4

Execute:   (a)  and

(b)  so

Evaluate:   The two tensions add up to 630 N, which is more than the traction force, because the cables do not pull directly along the spinal column.

5.5.	Identify:   Apply  to the frame.

Set Up:   Let w be the weight of the frame. Since the two wires make the same angle with the vertical, the tension is the same in each wire.

Execute:   The vertical component of the force due to the tension in each wire must be half of the weight, and this in turn is the tension multiplied by the cosine of the angle each wire makes with the vertical.  and

Evaluate:   If   and  as  Therefore, there must be an angle where

5.7.	Identify:   Apply  to the object and to the knot where the cords are joined.

Set Up:   Let  be upward and  be to the right.

Execute:   (a)  Since  adding the last two equations gives  and so  Then,

(b) Similar to part (a),  and

Adding these two equations,  and

Evaluate:   In part (a),  since only the vertical components of  and  hold the object against gravity. In part (b), since  has a downward component  is greater than w.

5.8.	Identify:   Apply Newton’s first law to the car.

Set Up:   Use x and y coordinates that are parallel and perpendicular to the ramp.

Execute:   (a) The free-body diagram for the car is given in Figure 5.8. The vertical weight w and the tension T in the cable have each been replaced by their x and y components.

(b)  gives  and

(c)  gives  and

Evaluate:   We could also use coordinates that are horizontal and vertical and would obtain the same values of n and T.

Figure 5.8

5.12.	Identify:   Apply Newton’s second law to the rocket plus its contents and to the power supply. Both the rocket and the power supply have the same acceleration.

Set Up:   The free-body diagrams for the rocket and for the power supply are given in Figures 5.12a and b. Since the highest altitude of the rocket is 120 m, it is near to the surface of the earth and there is a downward gravity force on each object. Let  be upward, since that is the direction of the acceleration. The power supply has mass

Execute:   (a)  applied to the rocket gives

(b)  applied to the power supply gives

Evaluate:   The acceleration is constant while the thrust is constant and the normal force is constant while the acceleration is constant. The altitude of 120 m is not used in the calculation.

Figure 5.12

5.13.	Identify:   Use the kinematic information to find the acceleration of the capsule and the stopping time. Use Newton’s second law to find the force F that the ground exerted on the capsule during the crash.

Set Up:   Let  be upward.  The free-body diagram for the capsule is given in Figure 5.13.

Execute:       gives

(b)  applied to the capsule gives  and

(c)  gives

Evaluate:   The upward force exerted by the ground is much larger than the weight of the capsule and stops the capsule in a short amount of time. After the capsule has come to rest, the ground still exerts a force mg on the capsule, but the large  force is exerted only for 0.0187 s.

Figure 5.13

5.14.	Identify:   Apply Newton’s second law to the three sleds taken together as a composite object and to each individual sled. All three sleds have the same horizontal acceleration a.

Set Up:   The free-body diagram for the three sleds taken as a composite object is given in Figure 5.14a and for each individual sled in Figure 5.14b–d. Let  be to the right, in the direction of the acceleration.

Execute:   (a)  for the three sleds as a composite object gives  and

(b)  applied to the 10.0 kg sled gives  and   applied to the 30.0 kg sled gives

Evaluate:   If we apply  to the 20.0 kg sled and calculate a from  and  found in part (b), we get   which agrees with the value we calculated in part (a).

Figure 5.14

5.15.	Identify:   Apply  to the load of bricks and to the counterweight. The tension is the same at each end of the rope. The rope pulls up with the same force  on the bricks and on the counterweight. The counterweight accelerates downward and the bricks accelerate upward; these accelerations have the same magnitude.

(a) Set Up:   The free-body diagrams for the bricks and counterweight are given in Figure 5.15.

Figure 5.15

(b) Execute:   Apply  to each object. The acceleration magnitude is the same for the two objects. For the bricks take  to be upward since  for the bricks is upward. For the counterweight 
take  to be downward since  is downward.

bricks:

counterweight:

Add these two equations to eliminate T:

(c)  gives

As a check, calculate T using the other equation.

gives  which checks.

Evaluate:   The tension is 1.30 times the weight of the bricks; this causes the bricks to accelerate upward. The tension is 0.696 times the weight of the counterweight; this causes the counterweight to accelerate downward. If   and  In this special case the objects don’t move. If   and  in this special case the counterweight is in free fall. Our general result is correct in these two special cases.

5.16.	Identify:   In part (a) use the kinematic information and the constant acceleration equations to calculate the acceleration of the ice. Then apply  In part (b) use  to find the acceleration and use this in the constant acceleration equations to find the final speed.

Set Up:   Figures 5.16a and b give the free-body diagrams for the ice both with and without friction. 
Let  be directed down the ramp, so  is perpendicular to the ramp surface. Let  be the angle between the ramp and the horizontal. The gravity force has been replaced by its x and y components.

Execute:   (a)     gives   gives  and

(b)  gives  and

Then    and  gives

Evaluate:   With friction present the speed at the bottom of the ramp is less.

Figure 5.16a, b

5.17.	Identify:   Apply  to each block. Each block has the same magnitude of acceleration a.

Set Up:   Assume the pulley is to the right of the 4.00 kg block. There is no friction force on the 4.00 kg block; the only force on it is the tension in the rope. The 4.00 kg block therefore accelerates to the right and the suspended block accelerates downward. Let  be to the right for the 4.00 kg block, so for it  and let  be downward for the suspended block, so for it

Execute:   (a) The free-body diagrams for each block are given in Figures 5.17a and b.

(b)  applied to the 4.00 kg block gives  and

(c)  applied to the suspended block gives  and

(d) The weight of the hanging block is  This is greater than the tension in the rope;

Evaluate:   Since the hanging block accelerates downward, the net force on this block must be downward and the weight of the hanging block must be greater than the tension in the rope. Note that the blocks accelerate no matter how small m is. It is not necessary to have  and in fact in this problem m is less than 4.00 kg.

Figure 5.17a, b

5.20.	Identify:   Apply  to the composite object of elevator plus student  and also to the student  The elevator and the student have the same acceleration.

Set Up:   Let  be upward. The free-body diagrams for the composite object and for the student are given in Figures 5.20a and b. T is the tension in the cable and n is the scale reading, the normal force the scale exerts on the student. The mass of the student is

Execute:   (a)  applied to the student gives   The elevator has a downward acceleration of

(b)

(c)  means  The student should worry; the elevator is in free fall.

(d)  applied to the composite object gives   In part (a),  In part (c),  and

Evaluate:   In part (b),  The weight of the composite object is 8330 N. When the acceleration is upward the tension is greater than the weight and when the acceleration is downward the tension is less than the weight.

Figure 5.20a, b

5.27.	(a) Identify:   Constant speed implies  Apply Newton’s first law to the box. The friction force is directed opposite to the motion of the box.

Set Up:   Consider the free-body diagram for the box, given in Figure 5.27a. Let  be the horizontal force applied by the worker. The friction is kinetic friction since the box is sliding along the surface.

|  |  | Execute: so |
| --- | --- | --- |
| Figure 5.27a |  |  |

(b) Identify:   Now the only horizontal force on the box is the kinetic friction force. Apply Newton’s second law to the box to calculate its acceleration. Once we have the acceleration, we can find the 
distance using a constant acceleration equation. The friction force is  just as in part (a).

Set Up:   The free-body diagram is sketched in Figure 5.27b.

|  |  | Execute: |
| --- | --- | --- |
| Figure 5.27b |  |  |

Use the constant acceleration equations to find the distance the box travels:

Evaluate:   The normal force is the component of force exerted by a surface perpendicular to the surface. Its magnitude is determined by  In this case n and mg are the only vertical forces and  so  Also note that  and n are proportional in magnitude but perpendicular in direction.

5.33.	Identify:   Use  to find the acceleration that can be given to the car by the kinetic friction force. Then use a constant acceleration equation.

Set Up:   Take  in the direction the car is moving.

Execute:   (a) The free-body diagram for the car is shown in Figure 5.33.  gives

gives   and  Then  and  gives

(b)

Evaluate:   For constant stopping distance  is constant and  is proportional to  The answer to part (b) can be calculated as

Figure 5.33

5.35.	Identify:   Apply  to each crate. The rope exerts force T to the right on crate A and force T to the left on crate B. The target variables are the forces T and F. Constant v implies

Set Up:   The free-body diagram for A is sketched in Figure 5.35a

|  |  | Execute: |
| --- | --- | --- |
| Figure 5.35a |  |  |

Set Up:   The free-body diagram for B is sketched in Figure 5.35b.

|  |  | Execute: |
| --- | --- | --- |
| Figure 5.35b |  |  |

Use the first equation to replace T in the second:

(a)

(b)

Evaluate:   We can also consider both crates together as a single object of mass   for this combined object gives  in agreement with our answer in part (a).

5.42.	Identify:   The acceleration of the car at the top and bottom is toward the center of the circle, and Newton’s second law applies to it.

Set Up:   Two forces are acting on the car, gravity and the normal force. At point B (the top), both forces are toward the center of the circle, so Newton’s second law gives  At point A (the bottom), gravity is downward but the normal force is upward, so

Execute:   Solving the equation at B for the acceleration gives  Solving the equation at A for the normal force gives

Evaluate:   The normal force at the bottom is greater than at the top because it must balance the weight in addition to accelerate the car toward the center of its track.

5.44.	Identify:   Since the car travels in an arc of a circle, it has acceleration  directed toward the center of the arc. The only horizontal force on the car is the static friction force exerted by the roadway. 
To calculate the minimum coefficient of friction that is required, set the static friction force equal to its maximum value,  Friction is static friction because the car is not sliding in the radial direction.

Set Up:   The free-body diagram for the car is given in Figure 5.44. The diagram assumes the center of the curve is to the left of the car.

Execute:    (a)  gives   gives   and

(b)  so

Evaluate:   A smaller coefficient of friction means a smaller maximum friction force, a smaller possible acceleration and therefore a smaller speed.

Figure 5.44

5.47.	Identify:   Apply  to the composite object of the person plus seat. This object moves in a horizontal circle and has acceleration  directed toward the center of the circle.

Set Up:   The free-body diagram for the composite object is given in Figure 5.47. Let  be to the right, in the direction of  Let  be upward. The radius of the circular path is  The total mass is  Since the rotation rate is  the period T is

Execute:    gives  and   gives  and

The tension in the horizontal cable is 8370 N and the tension in the other cable is 1410 N.

Evaluate:   The weight of the composite object is 1080 N. The tension in cable A is larger than this since its vertical component must equal the weight.  The tension in cable B is less than this because part of the required inward force comes from a component of the tension in cable A.

Figure 5.47

5.49.	Identify:   The acceleration due to circular motion is

Set Up:     is the number of revolutions per second.

Execute:   (a) Setting  and solving for the period T gives

so the number of revolutions per minute is

(b) The lower acceleration corresponds to a longer period, and hence a lower rotation rate, by a factor of the square root of the ratio of the accelerations,

Evaluate:   In part (a) the tangential speed of a point at the rim is given by  so  the space station is rotating rapidly.

5.50.	Identify:    The apparent weight of a person is the normal force exerted on him by the seat he is sitting on. His acceleration is  directed toward the center of the circle.

Set Up:    The period is  The passenger has mass

Execute:   (a)  Note that

(b) The free-body diagram for the person at the top of his path is given in Figure 5.50a. The acceleration is downward, so take  downward.  gives

The free-body diagram for the person at the bottom of his path is given in Figure 5.50b. The acceleration is upward, so take  upward.  gives  and

(c) Apparent weight means  and   and  The time for one revolution would be  Note that

(d)  twice his true weight.

Evaluate:   At the top of his path his apparent weight is less than his true weight and at the bottom of his path his apparent weight is greater than his true weight.

Figure 5.50a, b

5.51.	Identify:   Apply  to the motion of the pilot. The pilot moves in a vertical circle. The apparent weight is the normal force exerted on him. At each point  is directed toward the center of the circular path.

(a) Set Up:   “the pilot feels weightless” means that the vertical normal force n exerted on the pilot by 
the chair on which the pilot sits is zero. The force diagram for the pilot at the top of the path is given in Figure 5.51a.

|  |  | Execute: |
| --- | --- | --- |
| Figure 5.51a |  |  |

Thus

(b) Set Up:   The force diagram for the pilot at the bottom of the path is given in Figure 5.51b. Note that the vertical normal force exerted on the pilot by the chair on which the pilot sits is now upward.

|  |  | Execute: This normal force is the pilot’s apparent weight. |
| --- | --- | --- |
| Figure 5.51b |  |  |

so

Thus

Evaluate:   In part (b),  since the acceleration is upward. The pilot feels he is much heavier than when at rest. The speed is not constant, but it is still true that  at each point of the motion.

5.54.	Identify:   The ball has acceleration  directed toward the center of the circular path. When the ball is at the bottom of the swing, its acceleration is upward.

Set Up:   Take  upward, in the direction of the acceleration. The bowling ball has mass

Execute:   (a)  upward.

(b) The free-body diagram is given in Figure 5.54.  gives

Evaluate:   The acceleration is upward, so the net force is upward and the tension is greater than the weight.

Figure 5.54

5.56.	Identify:   Apply Newton’s first law to the person. Each half of the rope exerts a force on him, directed along the rope and equal to the tension T in the rope.

Set Up:   (a) The force diagram for the person is given in Figure 5.56.

|  |  | and are the tensions in each half of the rope. |
| --- | --- | --- |
| Figure 5.56 |  |  |

Execute:

This says that  (The tension is the same on both sides of the person.)

But  so

(b) The relation  still applies but now we are given that  (the breaking strength) and are asked to find

Evaluate:    says that  when  (rope is vertical).

when  since the upward component of the tension becomes a smaller fraction of the tension.

5.58.	Identify:   Apply  to each object. Constant speed means

Set Up:   The free-body diagrams are sketched in Figure 5.58.  is the tension in the lower chain,  is the tension in the upper chain and  is the tension in the rope.

Execute:   The tension in the lower chain balances the weight and so is equal to w. The lower pulley must have no net force on it, so twice the tension in the rope must be equal to w and the tension in the rope, which equals F, is  Then, the downward force on the upper pulley due to the rope is also w, and so the upper chain exerts a force w on the upper pulley, and the tension in the upper chain is also w.

Evaluate:   The pulley combination allows the worker to lift a weight w by applying a force of only

Figure 5.58

5.64.	Identify:   We can use the standard kinematics formulas because the force (and hence the acceleration) is constant, and we can use Newton’s second law to find the force needed to cause that acceleration. Kinetic friction, not static friction, is acting.

Set Up:   From kinematics, we have  and  applies. Forces perpendicular to the ramp balance. The force of kinetic friction is

Execute:   Call +x upward along the surface of the ramp. Kinematics gives   gives  Solving for F gives

Evalute:   As long as the box is moving, only kinetic friction, not static friction, acts on it. The force can be less than the weight of the box because only part of the box’s weight acts down the ramp.

5.66.	Identify:   The horizontal force has a component up the ramp and a component perpendicular to the surface of the ramp. The upward component causes the upward acceleration and the perpendicular component affects the normal force on the box. Newton’s second law applies. The forces perpendicular to the surface balance.

Set Up:   Balance forces perpendicular to the ramp:  Apply Newton’s second law parallel to the ramp surface:

Execute:   Using the above equations gives  The force of friction is  so   Solving for F gives  Putting in the numbers, we get

Evaluate:   Even though the push is horizontal, it can cause a vertical acceleration because it causes the normal force to have a vertical component greater than the vertical component of the box’s weight.

5.68.	Identify:   This is a system having constant acceleration, so we can use the standard kinematics formulas as well as Newton’s second law to find the unknown mass

Set Up:   Newton’s second law applies to each block. The standard kinematics formulas can be used to find the acceleration because the acceleration is constant. The normal force on  is  so the force of friction on it is

Execute:   Standard kinematics gives the acceleration of the system to be  so the friction force on  is  Applying Newton’s second law to  gives  where T is the tension in the cord. Solving for T gives  Newton’s second law for  gives  so

Evaluate:   This problem is similar to Problem 5.67, except for the sloped surface. As in that problem, we could treat these blocks as a two-block system. Newton’s second law would then give  which gives the same result as above.