Physics 103			Assignment 9

9.1.	Identify:    with  in radians.

Set Up:

Execute:   (a)

(b)

(c)

Evaluate:   An angle is the ratio of two lengths and is dimensionless. But, when  is used,  must be in radians. Or, if  is used to calculate the calculation gives  in radians.

9.2.	Identify:    since the angular velocity is constant.

Set Up:

Execute:   (a)

(b)

Evaluate:   In  we must use the same angular measure (radians, degrees or revolutions) for both  and

9.3.	Identify    Writing Eq. (2.16) in terms of angular quantities gives

Set Up:    and

Execute:   (a) A must have units of and B must have units of

(b)  (i) For   (ii) For

(c)  For  and

Evaluate:   Both  and  are positive and the angular speed is increasing.

9.8.	Identify:     When  is linear in t,  for the time interval  to  is

Set Up:   From the information given,

Execute:   (a) The angular acceleration is positive, since the angular velocity increases steadily from a negative value to a positive value.

(b) It takes 3.00 seconds for the wheel to stop  During this time its speed is decreasing. For the next 4.00 s its speed is increasing from

(c) The average angular velocity is   then leads to displacement of 7.00 rad after 7.00 s.

Evaluate:   When  and  have the same sign, the angular speed is increasing; this is the case for  to  When  and  have opposite signs, the angular speed is decreasing; this is the case between  and

9.9.	Identify:    Apply the constant angular acceleration equations.

Set Up:   Let the direction the wheel is rotating be positive.

Execute:   (a)

(b)

Evaluate:    the same as calculated with another equation in part (b).

9.11.	Identify:    Apply the constant angular acceleration equations to the motion. The target variables are t 
and

Set Up:   (a)   (starts from rest);

Execute:

(b)

Evaluate:   We could use  to calculate  which checks.

9.17.	Identify:   Apply Eq. (9.12) to relate  to

Set Up:   Establish a proportionality.

Execute:   From Eq. (9.12), with  the number of revolutions is proportional to the square of the initial angular velocity, so tripling the initial angular velocity increases the number of revolutions by 9, to 9.00 rev.

Evaluate:   We don’t have enough information to calculate  all we need to know is that it is constant.

9.21.	Identify:   Use constant acceleration equations to calculate the angular velocity at the end of two revolutions.

Set Up:

Execute:   (a)

(b)

Evaluate:    and  are completely equivalent expressions for

9.22.	Identify:    and

Set Up:   The linear acceleration of the bucket equals  for a point on the rim of the axle.

Execute:   (a)   gives

(b)

Evaluate:   In  and   and  must be in radians.

9.25.	Identify:   Use Eq. (9.15) and solve for r.

Set Up:    so  where  must be in rad/s

Execute:

Then

Evaluate:   The diameter is then 0.214 m, which is larger than 0.127 m, so the claim is not realistic.

9.31.	Identify:   Use Table 9.2. The correct expression to use in each case depends on the shape of the object and the location of the axis.

Set Up:   In each case express the mass in kg and the length in m, so the moment of inertia will be in

Execute:   (a) (i)

(ii)  (iii) For a very thin rod, all of the mass is at the axis and

(b) (i)

(ii)

(c) (i)

(ii)

Evaluate:   I depends on how the mass of the object is distributed relative to the axis.

9.33.	Identify:   I for the object is the sum of the values of I for each part.

Set Up:   For the bar, for an axis perpendicular to the bar, use the appropriate expression from Table 9.2. For a point mass,  where r is the distance of the mass from the axis.

Execute:   (a)

(b)

(c)  because all masses are on the axis.

(d) All the mass is a distance from the axis and

Evaluate:   I for an object depends on the location and direction of the axis.

9.41.	Identify:    Use Table 9.2 to calculate I.

Set Up:    For the moon,  and  The moon moves through  in 27.3 d.

Execute:   (a)

(b)  Considering the expense involved in tapping the moon’s rotational energy, this does not seem like a worthwhile scheme for only 158 years worth of energy.

Evaluate:   The moon has a very large amount of kinetic energy due to its motion. The earth has even more, but changing the rotation rate of the earth would change the length of a day.

9.43.	Identify:    with  in rad/s. Solve for I.

Set Up:

Execute:      and

Evaluate:   In  must be in rad/s.

9.47.	Identify:   Apply conservation of energy to the system of stone plus pulley.  relates the motion of the stone to the rotation of the pulley.

Set Up:   For a uniform solid disk,  Let point 1 be when the stone is at its initial position and point 2 be when it has descended the desired distance. Let  be upward and take  at the initial position of the stone, so  and  where h is the distance the stone descends.

Execute:   (a)    The stone has speed  The stone has kinetic energy   gives

(b)

Evaluate:   The gravitational potential energy of the pulley doesn’t change as it rotates. The tension in the wire does positive work on the pulley and negative work of the same magnitude on the stone, so no net work on the system.

9.55.	Identify and Set Up:   Use Eq. (9.19). The cm of the sheet is at its geometrical center. The object is sketched in Figure 9.55.

Execute:

|  |  | From part (c) of Table 9.2, The distance d of P from the cm is |
| --- | --- | --- |
| Figure 9.55 |  |  |

Thus

Evaluate:    For an axis through P mass is farther from the axis.

9.72.	Identify:   Use the constant angular acceleration equations, applied to the first revolution and to the first two revolutions.

Set Up:   Let the direction the disk is rotating be positive.  Let t be the time for the first revolution. The time for the first two revolutions is

Execute:   (a) applied to the first revolution and then to the first two revolutions gives and  Eliminating between these equations gives    The positive root is

(b) and gives

Evaluate:   At the start of the second revolution,  The distance the disk rotates in the next 0.750 s is   which is two revolutions.